## Slide 1: Interfacing LEDs to 8051 and displaying Binary Patterns
Engr. Shahzada Fahim Jan

## Slide 2: Looping in the 8051
Repeating a sequence of instruction certain number of times
Most widely used action that any microprocessor perform
In 8051, the loop action is performed by the instruction “DJNZ reg,label”
Register is decremented, if it is not zero, it jumps to the target address referred to by the label.
Register is loaded with the counter for the number of repititions

## Slide 3
MOV A,#0
MOV R2, #10
AGAIN: ADD A,#03
DJNZ R2,AGAIN
MOV R5,A
What is the maximum number of times that the loop can be repeated?

## Slide 4: Loop inside a loop
What happens if we want to repeat an action more times than 256?
To do that, we use a loop inside a loop
Nested loop
Here we use two registers
MOV A,#55H
MOV R3,#10
NEXT: MOV R2,#70
AGAIN: CPL A
DJNZ R2,AGAIN
DJNZ R3,NEXT

## Slide 5: Unconditional jump (SJMP)
2 byte instruction
First byte is the opcode
Second byte is the relative address of the target location
Range 00-FFH

## Slide 6: ACALL
ACALL is 2 byte instruction
Target address must be in 2k-byte address range
Processor automatically save the address of the instruction immediately below ACALL on the stack.
When a subroutine called, control is transferred to that subroutine
Upon executing RET it will resume back the execution in the caller
Every subroutine needs RET as the last instruction

## Slide 7
Lab Tasks
Run all the programs given in the lecture and attach the output
Display the pattern using assembly and C language
00000001
00000010
00000100
….
10000000
00000001
00000010